## Slide 1
SOCIAL ROBOTICS II:
Social Interactivity Mentor for Youth with Autism using the NAO Robot
(SIMYAN)
Andrew Nguyen, Bryce George, Colton Homuth, William Ross
Sponsor: Dr. Adham Atyabi
Faculty Sponsor: Mr. Bill Michael
December 4, 2020

## Slide 2: PROBLEM OVERVIEW
ASD impairs social interactions
Even more important to learn these skills while young
Social interactions are critical for future success
Robotics may be a key solution to developing these social skills

## Slide 3: PROBLEM BACKGROUND
We are developing the functionality for the robot to have social interactions with humans
Limited in our knowledge of literature on best approaches for social development in children with ASD - specific therapeutics are out of scope
Our work is more general in scope and guided by our sponsors prior research and guidance

## Slide 4
Coding Standards | Python PEP 8 formatting style Use 4 spaces instead of tabs Comments Describe all functions and their parameters References/links to supporting documentation (Optional) Custom utilities should provide a command line or GUI interface
Documentation Standards (GitHub) | Committed to UCCS-Social-Robotics/docs Must include a Wiki page or markdown for each module Include author(s) GitHub username and date information at the top of documentation files and wiki pages
STANDARDS DISCUSSION

## Slide 5: CONSTRAINTS
Put constraints here...

## Slide 6: LITERATURE SEARCH
Using social robots to work with ASD individuals is an emerging research field...
Commercial Robots for ASD Research and Therapy |  |  |  |  |  | 
Robot | Made By | Height (cm) | Ambulatory | Programmable | Degrees of Freedom | Features
Milo | Robokind | ~58 | Yes | Yes | 21 | Humanoid High degrees of freedom for body language expression Verbal emotive expression
NAO | SoftBank Robotics | 58 | Yes | Yes | 25 | 
QTrobot | LuxAI | 63 | No | Yes | 17 | 

## Slide 7: LITERATURE SEARCH
Used for teaching social skills
Body Language Cognition
Emotional Intelligence
Social Customs/Standards
Language Development
Self Expression
Facilitate researchers, educators, and therapists
ASD children more likely to interact with adult, asking questions to learn how to operate a robot
ASD individuals are calmer when interacting with robot than with person
Consistency of robot speech, movement, and interaction is comforting
Fewer distracting body language cues than a human
Used in:
Classrooms
Treatment Facilities
Research Facilities

## Slide 8: PROJECT SCOPE
Outside Scope
Not aiming to produce diagnostic test
Not aiming to create therapeutic experience
Not aiming to design or conduct a particular research experiment
Within Scope
Create a framework to aid the development and implementation of advanced behaviors to support diagnostic and therapeutic applications
Develop behavior components for a specific scenario as a POC
  Interactive drawing exercise with a human subject

## Slide 9: REQUIREMENTS ANALYSIS: ENVIRONMENT SURVEY
Frontier customer in emerging field
Limited existing research to draw upon
Using NAO robots provided by UCCS
Existing NAO Framework base
  Basic robot operation
  Support for some advanced behaviors
  Extensible via custom modules
Relatively small community using NAO
  Limited community contributions
  Less likely to find useful utilities already implemented
Image 1

## Slide 10: REQUIREMENTS ANALYSIS:
Needs
Extension of existing NAO framework
Advanced behaviors
  Cognition
  Speech
  Vision
  Mobility & Motor Control
Provide “play” experience
Opportunity to learn social cues and concepts
Human mannerisms and social characteristics
Wants
Relative autonomy
  Intelligence
  Adaptability
Natural interaction experience
  Intuitive
  Instructive
  Comfortable
Solution extensibility
Solution reusability
CUSTOMER
NEEDS & WANTS

## Slide 11: REQUIREMENTS ANALYSIS: CONSIDERATIONS
Complexity of human social environments
  Natural language processing
  Contextual reference
  Unexpected disruptions/interruptions
  Multiple human interactors
Environmental awareness
  Measuring 3D distance and depth in environment
  Recognizing obstacles and resources
  Mapping environment and moving to different locations
  Understanding of object properties
    Scale
    Orientation
    Color
Image 2

## Slide 12: REQUIREMENTS ANALYSIS: CONSIDERATIONS
Reasoning and Situational Analysis
  Situational Prediction
  Situational Responsiveness
  Data integration and interpretation
Deep Learning & AI
  Model development and training
    Accuracy
    Training Time
    Computational resources
  Model application
    Collecting necessary data
    Collecting sufficient data
    Processing data within acceptable timeframe

## Slide 13: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
1 | Load Master Module | Allocate all necessary resources and load the Activities Master Module Detect subject within 5m of starting position | Performed on robot startup Verbal notification of completion
2 | Initialize Activities Master Module | Verbally greet subject Orient face to look at subject Allocate/initialize all master level subroutines | Greet subject < 1s after detection

## Slide 14: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
3 | Start Activity | Verbally explain operation instructions Verify valid verbal activity selections Notify of invalid activity selections and re-prompt Discover all available activity modules Load and initialize selected activity module | Verify and acknowledge selections <= 1s after heard

## Slide 15: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
4 | Select Object to Draw | Verbally explain drawing activity Verbally list drawable objects Prompt for object selection Verify object selection Notify of invalid object selections and re-prompt | Verify and acknowledge selections <= 1s after heard

## Slide 16: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
5 | Obtain Writing Implement | Determine if already holding writing implement Ask whether to continue using current writing implement Drop writing implement Verify and acknowledge choice to use current writing implement Verbally instruct subject to provide new writing implement | Verify and acknowledge selections <=1s after heard

## Slide 17: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
5 | Obtain Writing Implement (continued) | Detect when to close hand to grip writing implement Close hand to grip writing implement Evaluate writing implement orientation Notify invalid orientation and instruct how to fix Evaluate if cap still on Notify cap still on and instruct subject to remove it | Detect writing implement in hand in <=1s after it is placed there Identify marker orientation <2s after closing grip Identify if cap is still on in <2s

## Slide 18: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
5 | Obtain Writing Implement (continued) | Determine writing implement color (black, blue, red, green, brown, purple, or yellow) Notify cap still on and instruct subject to remove it Determine writing implement color | 

## Slide 19: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
6 | Draw Object | Locate/detect drawing surface within 5m of position Notify of no drawing surface found and prompt for next action Detect drawing surface boundaries Notify inaccessible drawing surface conditions and instruct how to position correctly | Detect drawing surface in <= 3s Identify drawing surface boundaries in <= 1s

## Slide 20: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
6 | Draw Object (continued) | Load necessary hand/arm motor control module(s) Locate object drawing instructions Execute drawing instructions to draw the object on the drawing surface Able to draw square Four angles within +/- 1° of 90° Four sides same length to within +/- 5mm | 

## Slide 21: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
6 | Draw Object (continued) | Able to draw rectangle Four angles within +/- 1° of 90° Two sets of sides same length to within +/- 5mm Able to draw circle No segment of circumference varies by more than +/- 5% of radius length in distance from the center | 

## Slide 22: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
6 | Draw Object (continued) | Able to draw right triangle One angle +/-1° of 90° Two angles +/-1° of 45° Length of sides adjacent to 90° angle are same length within +/- 5mm | 

## Slide 23: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
7 | Interact with Subject | Select an appropriate user interaction statement Speak interaction statement to subject Listen for verbal response to an interrogative statement Evaluate response statement | Select or generate an interaction statement in <= 3s Evaluate a response statement in <= 3s

## Slide 24: REQUIREMENTS SPECIFICATIONS
# | Use Case | Functional Requirements | Quality of Service Requirements
8 | Complete Activity | Select an appropriate user interaction statement Speak interaction statement to subject Listen for verbal response to an interrogative statement Evaluate response statement | Select or generate an interaction statement in <= 3s Evaluate a response statement in <= 3s

## Slide 25: BLOCK DIAGRAM

## Slide 26: SYSTEM DESIGN EXPECTATIONS
Design will entail programing the NAO robot to draw with another person
Must supplement existing NAOqi API to perform more detailed tasks
  Handling a writing implement
  Recognizing a writing surface
  Intricate joint movement
  Social interaction
Since project is going to be implemented using NAO…
Majority of time will be spent developing/testing various algorithms
Most anticipated problems are standard problems with software development
  System integration
    Lots of tasks working simultaneously

## Slide 27: ISSUES
Minimal robotics experience
Minimal Python experience
Limited knowledge of Neural Networks and Machine Learning
Proprietary NAO Framework
Limited knowledge of ASD social behavior and therapies
COVID-19 closures and limitations

## Slide 28: TIMELINE
Setup Remote Access to Robot - TBD
Requirements Analysis Report - December 9, 2020
SDK Design - January ??, 2021
Drawing Module Design - February ??, 2021
Project Proposal Presentation - February ??, 2021
Integration with Jetson Nano GPU - February 28, 2021
Begin Development - February ??, 2021
Design Review Presentation - March ??, 2021
Finish Development - April ??, 2021
Integration Testing - April ??, 2021
End-to-End Testing - April ??, 2021
Presentation Preparation
Final Presentation - May ??, 2021

## Slide 29: DRAFT BUDGET
Items:
Jetson Nano GPU
Remote access equipment: Camera, “play pen” fence, padding
3d printed materials: utensil holder, backpack (for GPU)
Depth Sensor (Lidar/Infrared)
Cost allocation:
Jetson Nano GPU - free, borrowed from advisor Bill Michael
Depth Sensor ($300 maximum)
Remaining materials ($100 maximum)
*Funds will be acquired from department allowance of $100 per person

## Slide 30: CONCLUSION
Concluding remarks...

## Slide 31: REFERENCES
Images:
https://www.eduporium.com/media/catalog/product/cache/c687aa7517cf01e65c009f6943c2b1e9/n/a/nao-print_03_4.png
https://www.eduporium.com/media/catalog/product/cache/c687aa7517cf01e65c009f6943c2b1e9/n/a/nao-print_06_4.png

## Slide 32: ANY QUESTIONS?